Performance testing for HAProxy

CONTENTS

A. Different testing scenarios, hardware and software
      configurations.

B. Kernel tuning parameters

C. HAProxy/Nginx tuning

D. Test methodology and scripts

E. 10g/40g/baremetal/KVM testing results

F. Issues
A. Testing Scenarios, hardware and software
     configurations:

Testing scenarios:

Following testing measurements will be taken:

A.1 10g ethernet
A.1.1 Baremetal performance
A.2.1 KVM performance

A.2 40g ethernet
A.2.1 Baremetal performance

Hardware configurations:

Baremetal configuration:

CPU:	48 Intel(R) Xeon(R) CPU E5-2670 v3 @ 2.30GHz
Memory:	128 GB
NIC:	Intel Corporation 82599EB 10 Gigabit
NIC:	40g

KVM configuration:
CPU:	6 Intel(R) Xeon(R) CPU E5-2670 v3 @ 2.30GHz
Memory:	8 GB
NIC:	virtio-net (1, 2 queue configuration)

Software configurations:

Kernel version:	v3.9.6 (will move to 3.9.0 on new Ubuntu installation)
HAProxy:	v1.5.12
nginx:	v1.6.2
B. Kernel Tuning parameters for all nodes:

B.1 /etc/sysctl.conf

fs.file-max= 1048576
kernel.shmmax=8589934592
net.core.rmem_max=16777216
net.core.wmem_max=16777216
net.core.rmem_default=1048576
net.core.wmem_default=1048576
net.core.netdev_max_backlog=16384
net.core.somaxconn=32768
net.core.optmem_max=25165824
net.ipv4.tcp_rmem=4096 1048576 16777216
net.ipv4.tcp_wmem=4096 1048576 16777216
net.ipv4.tcp_max_syn_backlog=32768
vm.max_map_count=131060

# Huge pages for 2 VM's of 8GB each (increase proportionately)
# vm.nr_hugepages=9000
# vm.hugetlb_shm_group = 36

net.nf_conntrack_max=655360
net.netfilter.nf_conntrack_tcp_timeout_established=12000

B.2 /etc/security/limits.conf

Add these lines to increase file limits:
<user> soft nofile 786432
<user> hard nofile 1048576

For a haproxy server, the <user> field above is haproxy, while for a nginx server, it is www-data. To make this work for all nodes, add:
haproxy soft nofile 786432
haproxy hard nofile 1048576
www-data soft nofile 786432
www-data hard nofile 1048576
B.3 IRQ Bind and device tuning

The ixgbe cards support 48 TX/RX interrupts (same as the number of cpus
configured). Currently the systems run with all interrupts bound to CPU 0. This
needs to be changed so that irq0 is bound to cpu0, irq1 to cpu1, and so on. Use
set_irq_affinity.sh (David Miller) from:
https://gist.github.com/syuu1228/4352382

to set the irq's correctly. This sees a big gain in both latency (20%) and bandwidth
(50%) tests. Run on each node (can be kept in /etc/rc.local):
# set_irq_affinity.sh eth0

# Set GSO/GRO/SG/TSO on and LRO off:
ethtool -K eth0 gso on gro on sg on tso on lro off

rx-checksumming: on
tx-checksumming: on

Use Jumbo frame (9000 byte) for internal network.
C. HAProxy tuning:

3.1.d Bind HAProxy instances to difference CPU's: This results in another 5-10% gain for all workloads (see usage of cpu-map below).

3.2.1 Edit /etc/haproxy/haproxy.cfg and set these parameters:

3.2.1.a In the global section:
# Number of processes nbproc <= #cpus, not much improvement beyond 8
nbproc 6
maxconn 60000
tune.pipesize 524288
cpu-map 1 0
cpu-map 2 2
cpu-map 3 4
cpu-map 4 6
cpu-map 5 8
cpu-map 6 10

3.2.1.b In the defaults section:
        maxconn 60000
        option splice-auto
        option prefer-last-server
        timeout connect 5000ms
        timeout client 50000ms
        timeout server 50000ms

3.2.1.c In the backend section:
maxconn 60000
balance roundrobin
option prefer-last-server
option forwardfor
option splice-auto
cookie FKSID prefix indirect nocache
server nginx-1 <IP-backend1>:80 maxconn 30000 check
server nginx-2 <IP-backend2>:80 maxconn 30000 check
...
D. Nginx tuning:

3.3.1 Use the default configuration files, and edit /etc/nginx/nginx.conf and set these parameters:

3.3.1.a Add the following to the global part of the configuration file:

worker_processes=48; (or number of cpus)
worker_rlimit_nofile 16384;
worker_cpu_affinity=worker_cpu_affinity 000000000000000000000000000000000000000000000001 000000000000000000000000000000000000000000000010 000000000000000000000000000000000000000000000100 000000000000000000000000000000000000000000001000 000000000000000000000000000000000000000000010000 000000000000000000000000000000000000000000100000 000000000000000000000000000000000000000001000000 000000000000000000000000000000000000000010000000 000000000000000000000000000000000000000100000000
(this is based on the number of worker_threads, each worker is pinned to one cpu)

3.3.1.b In the Events section, add/change these parameters:
        worker_connections 16384;
        worker_aio_requests 1024;
        accept_mutex on;

3.3.1.c In the http section, add this at the top:
server {
        location / {
        root /var/www/html;
        }
        }
Note: Populate /var/www/html with static content

3.3.1.d In the http section, add/modify the following:
        sendfile on;
        tcp_nopush on;
        tcp_nodelay on;
        keepalive_requests 1000000;
        keepalive_timeout 65;

3.3.1.e Disable access log and turn on error log
access_log off;
error_log /var/log/nginx/error.log;
E. Test methodology and scripts

Use automated test scripts to run bandwidth and latency tests against HAProxy
from multiple clients. Bandwidth is defined as large response (4K and above),
while latency is defined as small packets (128 bytes – 1K).

E.1 Bandwidth tests on Baremetal:
E.1.1 No-SSL, Baremetal, 10g:
# ./run_test 172.20.232.67 80 1000000000 900 128K 20 10g 3

Bandwidth: 1195340.83 Kb/s ec = 9.11 Gb/sec
System utilization:
User: 3.40% Sys: 13.52% IRQ: 0% Softirq: 19.86% Idle: 63.21%
E.1.2 No-SSL, Baremetal, 40g:

E.1.3 SSL, Baremetal, 10g:
# ./run_test 172.20.232.67 443 1000000000 900 128K 20 10g 3
Bandwidth: 775990.81 Kb/s = 5.92 Gb/s
System utilization:
User: 26.25% Sys: 24.18% IRQ: 0% Softirq: 14.04% Idle: 35.51%

E.1.4 SSL, Baremetal, 40g:

E.2. Latency tests on Baremetal:
E2.1 No-SSL, Baremetal, 10g:
# ./run_test 172.20.232.67 80 1000000000 900 128 20 10g 3
Requests per second: 317263 operations/second
System utilization:
User: 23.67% Sys: 37.76% IRQ: 0% Softirq: 16.26% Idle: 22.30%

E2.2 No-SSL, Baremetal, 40g:

E2.3 SSL, Baremetal, 10g:
# ./run_test 172.20.232.67 443 1000000000 900 128 20 10g 3
Requests per second = 260708 operations/s
System utilization:
User: 34.15% Sys: 36.04% IRQ: 0% Softirq: 19.02% Idle: 10.77%

E2.4 SSL, Baremetal, 40g:

E.3 Bandwidth tests on KVM:

Changes:
1. (Host):
vm.nr_hugepages=9000
vm.hugetlb_shm_group = 36
2. (VM):
 2.1 haproxy.cfg:
cpu-map 0,1,2,3,4,5
 2.2 ethtool -L eth0 combined 4
 2.3 ifconfig eth0 mtu 9000

E.3.1 No-SSL, KVM – Single virtio-net queue, 10g:
# ./run_test 172.20.232.106 80 1000000000 900 128K 20 10g 3
Bandwidth: 806349 Kb/s = 6.15 Gb/s
System utilization:
User: 2.54% Sys: 7.70% IRQ: 0% Softirq: 14.50% Idle: 75.24%

E.3.2 SSL, KVM – Single virtio-net queue, 10g:
# ./run_test 172.20.232.106 443 1000000000 900 128K 20 10g 3
Bandwidth: 369894 Kb/s = 2.82 Gb/s
System utilization:
User: 79.52% Sys: 14.22% IRQ: 0% Softirq: 5.14% Idle: 1.09%

E.3.3 No-SSL, KVM – 4 virtio-net queue, 10g:
# ./run_test 172.20.232.106 80 1000000000 900 128K 20 10g 3
Bandwidth:	1131875 Kb/s = 8.63 Gb/s
System utilization:
User: 3.84% Sys: 19.78% IRQ: 0% Softirq: 18.74% Idle: 57.60%

E.3.4 SSL, KVM – 4 virtio-net queue, 10g:
# ./run_test 172.20.232.106 443 1000000000 900 128 20 10g 3
Bandwidth: 359696 Kb/s = 2.74 Gb/s
System utilization:
User: 77.61% Sys: 15.45% IRQ: 0% Softirq: 5.83% Idle: 1.10%
E.4 Latency tests on KVM:

E.4.1 No-SSL, KVM – Single virtio-net queue, 10g:
# ./run_test 172.20.232.106 80 1000000000 900 128 20 10g 3
Latency: 142573 Operations/sec
System utilization:
User: 12.13% Sys: 21.68% IRQ: 0% Softirq: 10.00% Idle: 56.16%

E.4.2 SSL, KVM – Single virtio-net queue, 10g:
# ./run_test 172.20.232.106 443 1000000000 900 128 20 10g 3
Latency: 136876 Operations/sec
System utilization:
User: 33.60% Sys: 21.30% IRQ: 0% Softirq: 8.82% Idle: 36.25%

E.4.3 No-SSL, KVM – 4 virtio-net queue, 10g:
# ./run_test 172.20.232.106 80 1000000000 900 128 20 10g 3
Latency: 285142 Operations/sec
System utilization:
User: 25.46% Sys: 39.70% IRQ: .01% Softirq: 20.15% Idle: 14.67%

E.4.4 SSL, KVM – 4 virtio-net queue, 10g:
# ./run_test 172.20.232.106 443 1000000000 900 128 20 10g 3
Latency: 200894 Operations/sec
System utilization:
User: 47.96% Sys: 31.91% IRQ: 0% Softirq: 17.71% Idle: 2.40%
Bandwidth Results

#	Description	BW / (gbps)	User%	Sys%	Softirq%	Idle%
1	No-SSL, BM, 10g	9.11	3.4	13.5	19.9	63.2
2	SSL, BM, 10g	5.92	26.3	24.2	14	35.5
3	No-SSL, KVM, 1vq	6.15	2.5	7.7	14.5	75.2
4	SSL, KVM, 1vq	2.82	79.5	14.2	5.1	1.1
5	No-SSL, KVM, 4vq	8.63	3.8	19.8	18.7	15.6
6	SSL, KVM, 4vq	2.74	77.6	15.5	5.8	1.1

(Maintainer says that he gets 4.6 gpbs on a 3.5GHz single core with AES-NI)

Much better result for SSL, KVM, 4vq by pinning vhost on different cpus from main
guest cpus, but on the same socket:

taskset -p -c 12,14,16,18,20,22 6649 (50, 51, 52)
Bandwidth: 3.54 Gb/s
User: 29.19% Sys: 44.63% IRQ: .02% Softirq: 14.65% Idle: 11.50% (Total: 99.99%)
4.72 Gb/s using procs=40 instead of 900
And 6.63 against BM for 40

Tuning irq on haproxy KVM improves more:
set_irq_affinity.sh with minor changes to support virtio0-input-
Without: 8.0 gbps (300K Latency)
With: 8.32 gbps (340K Latency, BM: 341K)
Latency Results

Description	Latency / (ops/sec)	User%	Sys%	Softirq%	Idle%
No-SSL, BM, 10g	341K	23.7	37.8	16.3	22.3
SSL, BM, 10g	260-303K	34.2	36.0	19.0	10.8
No-SSL, KVM, 1vq	143K	12.1	21.7	10.0	56.2
SSL, KVM, 1vq	137K	33.6	21.3	8.8	36.3
No-SSL, KVM, 4vq	340K with opt	25.5	39.7	20.2	14.7
SSL, KVM, 4vq	251K	48.0	32.0	17.7	2.4

Can get 256K in SSL, KVM, 4vq case by above tuning (pin vhost)
Vhost (without using hyperthreaded cpus), SSL latency test & no-SSL latency test:
Using same cpus as qemu: 145K 162K
Using different even cpus as qemu: 265K 324K (340K for 500)
Using all even cpus: 240K 270K
Using all odd cpus: 232K 296K
Using all cpus:	250K 288K
Using 12-46 evens: 227K 280K

Best: “Using different even cpus as qemu” (12,14,16,18,20,22)
F. Issues

Following are the issues found during testing:

F.1. SSL performance is low
F.1.1 For BW, the numbers for baremetal is about
   35% lower than for plain text.
F.1.2 For BW, the numbers for VM is even lower
    (need to investigate this).
F.1.3 Latency seems reasonable.

F.2 SSL for large I/O does not complete during testing and
stops at 90% completion. Workloads upto 16K
        complete but 128K does not complete. Working with
the community for a solution.